## Slide 1: 操作系统
操作系统是软件，是一个程序,它运行在监督管理状态
可以访问物理地址
访问特殊寄存器 (比如页表寄存器)
还有I/O设备等.
而普通程序在USER状态下运行
仅通过页表访问虚拟地址
通常无法访问IO设备
程序向操作系统请求服务（syscall）
给我更多的内存
从磁盘读取/写入数据
将像素放在屏幕上
给我键盘上的下一个字符

## Slide 2: 操作系统的层次
Hardware
Registers
ALUs
PCs
Caches
Kernel
Operating System
Applications
Device Drivers
Scheduler
Process Control Blocks (PCBs)
Page Tables
操作系统是将计算机各个部分粘合起来的胶水。
在竞争请求之间进行调解
解析名称/绑定
维护秩序/公平
Kernel 内核-O/S驻留的一部分处理最常见和最基本的服务请求。
Network Interfaces
Security
File system
Shared Device Libraries Queues
Word Processors
Graphical User
Interface (GUI)
Games
Spread Sheets
Web
Browser

## Slide 3: 操作系统的执行
操作系统为所有运行的程序建立一个进程表，包括
可执行内存的硬盘位置
页表位置、优先权
当前状态(正在运行, 等待准备, 等待事件, etc.)
PID (进程编号 ID) --分配给进程的一个数字编号
进程是一个独立的在自己内存空间运行的程序
操作系统在进程表里分配新的项目，为新的进程建立页表

## Slide 4: 页表初始化
foo
swap
0x00000000 | 0 | text segment
0x00001000 | 0 | text segment
0x00002000 | 1 | data segment
0x00003000 |  | 
0x00004000 |  | 
0x00005000 |  | 
0xffffe000 |  | 
0xfffff000 | 1 | stack
memory
disk
foo
page table

## Slide 5: 程序启动
现在一切都准备好了
进程表条目已设置
进程的PAGE TABLE已初始化
代码段在磁盘上，数据段在内存中，堆栈段已分配1页
操作系统已准备好，
一次只能运行一个程序，当某个程序正在运行时，程序获得权限，但操作系统保持控制权，当程序执行非法操作或计时器关闭时操作系统可以重新拿回控制权。
比如，当我们分支指令跳到“main”的开头时，出现页面错误，操作系统复制主代码的第一页到内存中的空闲页

## Slide 6: 代码中的页面错误
foo
swap
0x00000000 | 1 | text segment
0x00001000 | 0 | text segment
0x00002000 | 1 | data segment
0x00003000 |  | 
0x00004000 |  | 
0x00005000 |  | 
0xffffe000 |  | 
0xfffff000 | 1 | stack
memory
disk
foo
page table

## Slide 7: MIPS Exceptions
Reset 复位
Hardware Errors (Bus Error, Cache Error) 硬件错误
External Interrupt (6 inputs) 外部中断申请
Address Error 地址错误
Reserved Instruction 保留指令
TLB Miss System Call 快表缺失Breakpoint Trap 断点
Integer Overflow 整数溢出
Floating Point Error 浮点数出错
Timer 定时器出错
And a few more ….

## Slide 8: 异常处理
EPC 根据出错类型存储出错指令地址或下一条指令
转换到监控管理模式
跳到异常处理地址
PC FFFF FFFF BFC0 0000 for Reset
PC FFFF FFFF BFC0 0300 for Hardware error
PC FFFF FFFF BFC0 0380 for external interrupts
PC FFFF FFFF BFC0 0400 for …
保存寄存器内容
检查 “cause” register，判断异常原因
根据原因进行处理，跳到处理程序

## Slide 9
Graphics
Exp Bus
Xface
Base
I/O
LAN
SCSI
DRAM
VRAM
Processor
Cache/DRAM
Controller
Audio
Motion
Video
VRAM
DRAM
Cache
VRAM
DRAM
PCI Bus
ISA/EISA - MicroChannel
Add-in board
Bridge Architecture
个人计算机剖视

## Slide 10: 处理器I/O接口
处理器接口
  中断
  存储器映射I/O
I/O控制结构
  轮询（Polling）
  中断（Interrupts）
  直接存储器访问（DMA）
  I/O控制器
  I/O处理器
容量、访问时间、带宽
互联
  总线

## Slide 11
动机: 谁关心I/O?
CPU性能: 每年增长60%
I/O系统的性能受到机械延迟的限制(磁盘I/O)
  每年改进 < 10% (每秒的输入输出量 或 MB/sec)
Amdahl定律：系统加速比受制于最慢的部分！
  10% IO & 10x CPU => 性能改进 5倍 (损失50%)
  10% IO & 100x CPU => 性能改进10倍 (损失90%)
I/O瓶颈：
  缩小程序执行中 CPU部分的时间
  削减快速CPU的潜在性能

## Slide 12: I/O 系统设计的论题
  性能
  可扩展性（Expandability）
  失效时，可用性
Network
Disk
Processor
Cache
Memory - I/O Bus
Main
Memory
I/O
Controller
Disk
I/O
Controller
I/O
Controller
Graphics
interrupts
Notes: This is a more in-depth picture of the I/O system of a typical computer.
The I/O devices are shown here to be connected to the computer via I/O controllers that sit on the Memory I/O busses. We will talk about buses on Friday.
For now, notice that I/O system is inherently more irregular than the Processor and the Memory system because all the different devices (disk, graphics) that can attach to it.
So when one designs an I/O system, performance is still an important consideration.
But besides raw performance, one also has to think about expandability and resilience in the face of failure.
For example, one has to ask questions such as:
(a)[Expandability]: is there any easy way to connect another disk to the system?
(b) And if this I/O controller (network) fails, is it going to affect the rest of the network?
+2 = 7 min (X:47)

## Slide 13: 操作系统的职责
操作系统可以被看为以下两部分的接口：
  I/O硬件 与 请求 I/O的程序
I/O系统的三大特征：
  I/O系统被使用该处理器的多个程序共享
  I/O系统通常使用中断（外部产生的意外事件） 来通信有关 I/O操作的信息
    中断必须由操作系统处理，中断将导致系统进入管态（supervisor mode）
  对 I/O设备的低级控制非常复杂：
    管理一组并发事件 正确控制设备的需求必须非常详细
Notes: The OS acts as the interface between the I/O hardware and the program that requests I/O.
The responsibilities of the operating system arise from 3 characteristics of the I/O systems:
(a) First the I/O system is shared by multiple programs using the processor.
(b) I/O system, as I will show you, often use interrupts to communicate information about I/O operation and interrupt must be handled by the OS.
(c) Finally, the low-level control of an I/O device is very complex so we should leave to those crazy kernel programers to handle them.
+1 = 52 min. (Y:32)

## Slide 14: 对操作系统的需求
对共享I/O资源提供保护
  保证用户程序只能访问该用户有权访问的那部分I/O设备
提供访问设备的一种抽象：
  提供处理低级设备操作的例程
处理I/O设备产生的中断
提供公平访问共享I/O资源的策略
  所有用户程序必须平等访问I/O资源
对访问进行调度以求增大系统的吞吐率
Notes: Here is a list of the function the OS must provide. First it must guarantee that a user’s program can only access the portion of an I/O device that it has the right to do so.
Then the OS must hide low level complexity from the user by suppling routines that handle low-level device operation.
The OS also needs to handle the interrupts generated by I/O devices.
And the OS must be be fair: all user programs must have equal access to the I/O resources.
Finally, the OS needs to schedule accesses in a way that system throughput is enhanced.
+1 = 53 min. (Y:33)

## Slide 15: OS和I/O系统通信需求
操作系统必须能够防止：
  用户程序与 I/O设备之间的直接通信
如果用户程序能够直接对I/O进行操作，那么
  就不能提供对共享I/O资源的保护了。
需要三种类型的通信：
  OS必须能够给I/O设备提供命令
  当 I/O 设备完成操作或遇到错误时，它必须能够通报OS。
  数据必须在存储器和I/O设备之间传输
Notes: The OS must be able to communicate with the I/O system but at the same time, the OS must be able to prevent the user from communicating with the I/O device directly.
Why? Because if user programs could perform I/O directly, we would not be able to provide protection to the shared I/O device.
Three types of communications are required:
(1) First the OS must be able to give commands to the I/O devices.
(2) Secondly, the device e must be able to notify the OS when the I/O device has completed an operation or has encountered an error.
(3) Data must be transferred between memory and an I/O device.
+2 = 55 min. (Y:35)

## Slide 16: 给 I/O设备发送命令
可以使用两种方式对I/O设备寻址：
  专用 I/O指令
  存储器映像 I/O
专用 I/O指令指明：设备号 和 命令字
    设备号：处理器通过一组连线（这组连线是I/O总线的一部分）与设备进行通信
    命令字：它通常在总线的数据线上发送
存储器映像 I/O：
  地址空间的一部分分配给I/O设备
  对这些地址进行读和写就被解释为对给I/O设备的命令
  防止用户程序直接发送I/O 操作：
    I/O地址空间受到地址变换机制的保护
Notes: How do the OS give commands to the I/O device? There are two methods. Special I/O instructions and memory-mapped I/O.
If special I/O instructions are used, the OS will use the I/O instruction to specify both the device number and the command word.
The processor then executes the special I/O instruction by passing the device number to the I/O device (in most cases) via a set of control lines on the bus and at the same time sends the command to the I/O device using the bus’s data lines.
Special I/O instructions are not used that widely. Most processors use memory-mapped I/O where portions of the address space are assigned to the I/O device.
Read and write to this special address space are interpreted by the memory controller as I/O commands and the memory controller will do right thing to communicate with the I/O device
Why is memory-mapeed I/O so popular? Well, it is popular because we can use the same protection mechanism we already implemented for virtual memory to prevent the user from issuing commands to the I/O device directly.
+2 = 57 min. (Y:37)

## Slide 17: I/O 接口
独立I/O总线
CPU
Interface
Interface
Peripheral
Peripheral
Memory
存储器总线
独立的I/O指令 (in,out)
CPU
Interface
Interface
Peripheral
Peripheral
Memory
I/O和存储器传输的联线不同
公共存储器
& I/O总线
VME bus
Multibus-II
40 Mbytes/sec
（乐观）
MIPS 处理器
使该总线完全饱和!

## Slide 18: 存储器映射 I/O
ROM
RAM
I/O
单存储器&I/O总线
没有独立的I/O指令
CPU
Interface
Interface
Peripheral
Peripheral
Memory
$
CPU
L2 $
存储器总线
Memory
Bus Adaptor
I/O 总线

## Slide 19: I/O 设备通报 OS
当发生下列情况时。OS需要知道：
  I/O设备完成了某一操作
  I/O操作遇到了错误
可以通过两种不同的方式实现：
  轮询（Polling）：
    I/O设备将信息放置在状态寄存器中；
    OS定期检测状态寄存器
  I/O中断：
    每当 I/O 设备需要处理器关注时，它就中断处理器继续进行正在处理的工作。
Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when:
(a) The I/O device has completed the operation.
(b) Or when the I/O device has encountered an error.
This can be accomplished in two different ways: Polling and I/O interrupt.
+1 = 58 min. (Y:38)

## Slide 20: 可编程I/O (轮询）
CPU
IOC
device
Memory
数据是否
准备好?
读数据
存数据
yes
no
done?
no
yes
若忙就循环等待
不能很有效地利用
除非设备非常快！
但需要不断检测 I/O
I/O工作可以分散到
计算代码之中

## Slide 21
CPU
flag
data
INTERFACE
DEVICE
loop: lw | $t0, flag($t1) | # | $t1 points to a
beq | $t0,$0,loop | # | keyboard structure
lw … | $t0, data($t1) | # | process keystroke
问题:
浪费 ， CPU 不断查询等待
系统模块性差：运行程序必须了解所有设备。
即使设备空闲，也会占用CPU周期！
应用代码直接处理I/O (eg, 忙等待):
KEY HIT : Flag1, Data  ASCII
“kb->flag” and
“kb->data” are just memory locations
Assumes:
typedef struct Device { int flag, data;
} Keyboard;
可编程Polled I/O (轮询）

## Slide 22: I/O中断
I/O中断就像一般的意外事件，只是：
  I/O中断是异步的
  需要进一步传送信息
相对于指令执行而言， I/O中断是异步的：
  I/O中断并不与任何指令相关联
  I/O中断并不防止任何指令继续执行
    我们可以在我们自己认为合适的时候处理这种中断
I/O中断比一般意外事件更加复杂：
  需要传达产生中断的设备的身份信息
  中断请求具有不同的紧急性
    需要对中断请求优先排队
Notes: How does an I/O interrupt different from the exception you already learned?
Well, an I/O interrupt is asynchronous with respect to the instruction execution while exception such as overflow or page fault are always associated with a certain instruction.
Also for exception, the only information needs to be conveyed is the fact that an exceptional condition has occurred but for interrupt, there is more information to be conveyed.
Let me elaborate on each of these two points.
Unlike exception, which is always associated with an instruction, interrupt is not associated with any instruction. The user program is just doing its things when an I/O interrupt occurs.
So I/O interrupt does not prevent any instruction from completing so you can pick your own convenient point to take the interrupt.
As far as conveying more information is concerned, the interrupt detection hardware must somehow let the OS know who is causing the interrupt.
Furthermore, interrupt requests needs to be prioritized. The hardware that can do all these looks like this.
+2 = 64 min. (Y:44)

## Slide 23: 中断逻辑
检测和对中断请求同步
  忽略被废止的中断 (masked off)
  对未决的中断请求排序
  创建中断微序列地址（ microsequence address）
  对中断微序列提供信号
Synchronizer
Circuits
Async
interrupt
requests
Interrupt Mask Reg
Interrupt
Priority
Network
uSeq.
addr &
select
logic
D
Q
D
Q
Async.
Inputs
Sync.
Inputs
Clk
Clk
:
:
Notes: First the interrupt requests have to pass through a synchronizer circuit, basically two flip flops in series, to avoid getting into meta-stability.
Then based on the contents of the interrupt mask registers, all the interrupts that are currently disabled are ignored.
The rest of the interrupt requests are then prioritized and we will generate the interrupt target address based on the highest priority interrupt we received.
+2 = 66 min. (Y:46)

## Slide 24: 程序中断/意外事件硬件
硬件中断服务：
  保存 PC (或在流水机器中多个 PC值)
  抑制正在被处理的中断
  转移到中断服务例程
  选项：
    保存状态、保存寄存器、保存中断信息
    改变状态、改变操作模式、获取中断信息
I/O中断的一个有利特点：
  异步性：不与指定指令相关联
  可以在流水线的最方便的时候来处理它！
Notes: Besides detecting the interrupt and generate the interrupt target address, what else does the hardware needs to do.
Well, at the minimum, the processor has to save the program counter or in a pipeline machine with delayed branch, you may have to save multiple program counters.
To prevent recursion within a interrupt service routine, the processor must also disable further interrupt from the device it is servicing. This can be done easily by turning the interrupt bit in the mask register off.
Then, the processor also has to branch to the interrupt target address. These (first three) are the things the hardware must do. Here are a list of optional things.
Well, as I said before, one good thing about the interrupt is that it is asynchronous so you can pick the most convenient place in the pipeline to take it.
+2 = 68 min. (Y:48)

## Slide 25: 从程序员来看
中断目标地址选项：
  通用：转移到所有中断的公共地址，然后软件对原因进行译码并指出下一步做什么
  专用：根据中断类型和/或级别自动转移到不同的地址—向量化中断
Add
Sub
Div
main
program
Service the
(keyboard)
interrupt
Save processor
status/state
Restore processor
status/state
(3) get PC
interrupts request (e.g., from keyboard)
(1)
(2) Save PC and “branch” to interrupt target address
Notes: Let me show you what I mean. For example here, the CPU receives a keyboard interrupt request in the middle of the Divide instruction.
If the divide instruction causes an divide by 0 exception , we have to handle it immediately.
But here we have an interrupt, we can say, well, I have been spending all this time doing this divide and is almost finish, let’s wait.
So the interrupt is not taken until after the divide instruction has completed.
As far as generating the interrupt target address is concerned, we also have two options.
First is the low cost version. We make all interrupts go to a common address and let the software to figure out what to do next.
Then for those you like to built complicated hardware, you can make the hardware automatically branch to different addresses based on the interrupt type and/or level.
This is called vectored interrupt.
+2 = 70 min. (Y:50)

## Slide 26: 中断驱动数据传输
CPU
IOC
device
Memory
add
sub
and
or
nop
read
store
...
rti
存储器
用户程序
(1) I/O中断
(2) 保存PC
(3) 中断服务地址
中断
服务
例程
(4)
设备传输率 = 10 MBytes/sec => 0 .1 x 10-6 sec/byte => 0.1 sec/byte
=> 1000 bytes = 100 sec
1000次传输 x 100 sec = 100 ms = 0.1 CPU seconds
用户程序仅在实际传输中才暂停
以每1ms一次的速率传输1000次：
1000次中断（每2微秒一次中断）
1000次中断服务（每次98微秒） = 0.1 CPU秒
离设备传输率还有很大空间！中断开销的1/2

## Slide 27: 把CPU从I/O处理中解放出来：DMA
Direct Memory Access (DMA):
  直接内存数据传送
  由外部控制器接管总线，内存传送数据块，不用CPU参与。
CPU
IOC
device
Memory
DMAC
CPU 向DMAC数据直接传送控制器送起始地址,
传送方向, 数据长度计数 . "start".
DMAC 向外设发送联络信号，向内存
发送联络信号、地址等.
Notes: Finally, lets see how we can delegate some of the I/O responsibilities from the CPU.
The first option is Direct Memory Access which take advantage of the fact that I/O events often involve block transfer: you are not going to access the disk 1 byte at a time.
The DMA controller is external to the processor and can acts as a bus master to transfer blocks of data to or from memory and the I/O device without CPU intervention.
This is how it works. The CPU sends the starting address, the direction and length of the transfer to the DMA controller and issues a start command.
The DMA controller then take over from there and provides handshake signals required (point to the last text block) to complete the entire block transfer.
So the DMA controller are pretty intelligent. If you add more intelligent to the DMA controller, you will end up with a IO processor or IOP for short.
+2 = 72 min. (Y:52)

## Slide 28: 直接存储器访问（DMA）
CPU
IOC
device
Memory
DMAC
以每毫秒一次的速率完成1000次传输的时间：
1 DMA建立时间 50 sec
1 次中断 2 sec
1 次中断服务 48 sec
0.0001 秒的CPU时间
CPU向DMAC发送开始地址、方向 ；
然后，发射“开始”命令。
DMAC 向外设控制器提供握手信号，
向存储器提供存储地址和握手信号
0
ROM
RAM
Peripherals
DMAC
n
存储器映射 I/O

## Slide 29: 把CPU从I/O处理中解放出来：IOP
CPU
IOP
Mem
D1
D2
Dn
. . .
main memory
bus
I/O
bus
CPU
IOP
(1) Issues
instruction
to IOP
memory
(2)
(3)
IOP非常智能，CPU只需发出一条简单的指令（Op、Device、Address），告诉他们目标设备是什么，以及在哪里可以找到更多命令（Addr）。IOP随后将从内存中获取诸如this（OP、Addr、Cnt、Other）之类的命令，并在I/O设备和内存系统之间进行所有必要的数据传输。IOP将在后台进行传输，它不会影响CPU.
因为它只有在CPU不使用内存时才会访问内存：这称为窃取内存周期。
OP Device Address
target device
where cmnds are
IOP looks in memory for commands
OP Addr Cnt Other
what
to do
where
to put
data
how
much
special
requests
(4) IOP interrupts
CPU when done
Notes: The IOP is so smart that the CPU only needs to issue a simple instruction (Op, Device, Address) that tells them what is the target device and where to find more commands (Addr).
The IOP will then fetch commands such as this (OP, Addr, Cnt, Other) from memory and do all the necessary data transfer between the I/O device and the memory system.
The IOP will do the transfer at the background and it will not affect the CPU because it will access the memory only when the CPU is not using it: this is called stealing memory cycles.
Only when the IOP finishes its operation will it interrupts the CPU.
+2 = 74 min. (Y:54)

## Slide 30: 输入/输出处理器
CPU
IOP
Mem
D1
D2
Dn
. . .
主存总线
I/O
总线
CPU
IOP
向 IOP发射指令
完成后中断
(1)
存储器
(2)
(3)
(4)
设备 与 存储器之间的数据传送由IOP直接控制
IOP 偷取 存储器周期
OP Device Address
目标设备
命令在哪里
在存储器中查找命令
OP Addr Cnt Other
做什么
数据放在哪里
多少
特殊请求

## Slide 31: I/O设备的类型和特征
行为：一个 I/O设备如何工作?
  输入设备：只读
  输出设备：只写，不能读
  存贮设备：可以重读，通常也可重写
合作对象：
  在I/O设备的另一方要么是人，要么是机器
  要么是输入设备传入数据，要么是输出设备读取数据
数据传输率
  数据可以传送的最大速率
    在I/O设备和主存之间
    或者 在I/O设备与CPU之间
Notes: Although there are many different I/O devices, they can all be organized based on these three characteristics: behavior, partner, and data rate.
Behavior deals with how an I/O device behave? Is it an input device such as a mouse? Or is it an output only device such as a printer? Or is it a storage device such as the disk.
Partner deals with what an I/O device interact? Does it interact with human or machine?
Finally data rate deals with the peak rate at which data can be transferred between the I/O device and the main memory or between the I/O device and the CPU.
+1 = 26 min. (Y:06)

## Slide 32
I/O 设备实例
设备 行为 合作方 数据传输率 (KB/sec)
键盘 输入 人 0.01
鼠标 输入 人 0.02
行式打印机 输出 人 1.00
激光打印机 输出 人 100.00
图形显示器 输出 人 30,000.00
LAN 输入或输出 机器 200.00
软盘 存贮 机器 50.00
光盘 存贮 机器 500.00
磁盘 存贮 机器 2,000.00

## Slide 33: 存贮设备: 磁盘
扇区（Sector）
磁道（Track）
柱面（Cylinder）
磁头（Head）
盘片（Platter）
用途
  长期、非易失的存贮
  在存贮层次中，大容量、廉价、较慢的级别
特性
  寻道时间(平均8 ms左右)
    定位延迟（positional latency）
    旋转延迟（rotational latency）
传输率
  大约每毫秒一个扇区 (5-15 MB/s)
  成块
容量
  Gigabytes
  三年四倍
7200 RPM = 120 RPS => 8 ms per rev
ave rot. latency = 4 ms
128 sectors per track => 0.25 ms per sector
1 KB per sector => 16 MB / s
响应时间
= 排队 + 控制器 + 寻道 + 旋转 + 传输
服务时间
Notes: The purpose of the magnetic disk is to provide long term, non-volatile storage. Disks are large in terms of capacity, inexpensive, but slow so they reside at the lowest level in the memory hierarchy.
There are 2 types of disks: floppy and hard drives. Both types relay on a rotating platter coasted with a magnetic surface and a movable head is used to access the disk.
The advantages of hard disks over floppy disks are:
(a) Platters are made of metal or glass so they are more rigid and can be larger.
(b) Hard disk also has higher density because it can be controlled more precisely.
(c) Hard disk also has higher data rate because it can spin faster.
(d) Finally, each hard disk drive can incorporate more than one platter.
+2 = 30 min. (Y:10)

## Slide 34: 磁盘的组织
典型数据 (依赖于磁盘大小)：
  每面500 至 2,000 磁道
  每道 32 至 128 扇区
    扇区是可以读写的最小单位
通常，所有磁道包含相同数量的扇区
恒定位密度：在外围磁道可以记录更多的扇区
盘片（Platters）
磁道（Track）
扇区（Sector）
Notes: Here is a primitive picture showing you how a disk drive can have multiple platters.
Each surface on the platter are divided into tracks and each track is further divided into sectors. A sector is the smallest unit that can be read or written.
By simple geometry you know the outer track have more area and you would thing the outer tack will have more sectors.
This, however, is not the case in traditional disk design where all tracks have the same number of sectors. Well, you will say, this is dumb but dumb is the reason they do it .
By keeping the number of sectors the same, the disk controller hardware and software can be dumb and does not have to know which track has how many sectors.
With more intelligent disk controller hardware and software, it is getting more popular to record more sectors on the outer tracks. This is referred to as constant bit density.
+2 = 32 min. (Y:12)

## Slide 35
磁盘的响应延迟
磁盘响应延迟 = 排队时间 + 控制器时间 +
寻道时间 + 旋转时间 + 传输时间
4K字节数据的传输：
寻道：8 ms以下
旋转：4.2 ms @ 7200 rpm
传输：1 ms @ 7200 rpm
盘片
磁头
扇区
驱动器
驱动臂
内磁道
外磁道

## Slide 36: 磁盘特性
读/写数据过程包括三个阶段：
  寻道时间：将盘臂定位到正确的磁道上
  旋转时间：旋转盘片，使得所需的扇区位于读/写磁头下；
  传输时间：传输读写磁头下的一块位流（扇区）
工业界报告的平均寻道时间：
  通常为：8 ms 至 12 ms
  (所有可能寻道的时间总和) / (所有可能的寻道情况总数)
由于磁盘访问的局部性，通常实际的寻道时间为：
  仅为广告数值的 25% 至 33%
Cylinder
Sector
Track
Head
Platter
柱面：在给定时刻所有盘面的所有位于磁头下面的磁道所构成的柱面
Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface.
The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces.
To access data, the operating system must direct the disk through a 3-stage process.
(a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time.
(b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency.
(c) Finally, once the desired sector is under the read/write head, the data transfer can begin.
The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks.
This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published.
+2 = 34 min. (Y:14)

## Slide 37: 旋转时间和传输时间
旋转时间
  大多数磁盘的转速为 3,600 至 7200 RPM
  每转动一周约需要 16 ms 至 8 ms
  每转动半周所需时间为 8 ms 至 4 ms
传输时间是下列参数的函数：
  传输大小(通常为一个扇区)： 1 KB / sector
  旋转速度： 3600 RPM 至 7200 RPM
  记录密度：一个磁道上每英寸记录的位数
  典型数值：每秒 2 至 12 MB
Notes: As far as rotational latency is concerned, most disks rotate at 3,600 RPM or approximately 16 ms per revolution.
Since on average, the information you desired is half way around the disk, the average rotational latency will be 8ms.
The transfer time is a function of transfer size, rotation speed, and recording density.
The typical transfer speed is 2 to 4 MB per second.
Notice that the transfer time is much faster than the rotational latency and seek time.
This is similar to the DRAM situation where the DRAM access time is much shorter than the DRAM cycle time.
***** Do anybody remember what we did to take advantage of the short access time versus cycle time? Well, we interleave!
+2 = 36 min. (Y:16)

## Slide 38: Magnetic Disks: Outside

## Slide 39: Inside

## Slide 40: Platters and Heads

## Slide 41: 存贮技术的驱动力
主流计算模式的驱动
  五十年代: 批处理 到 在线处理 的转变
  九十年代: 集中处理 到 普及计算 的转变
    计算机无处不在：电话、电子书籍、汽车、摄像机
    全球性光纤网络及无线网络
存贮工业的成效：
  嵌入式存贮
    更小、更便宜、更可靠、更低功耗
  数据使用
    高容量、层次式管理存储系统

## Slide 42: 可靠性 与 可用性 （Reliability and Availability）
常被混淆的两个概念
  可靠性：是否有部件失效？
  可用性：是否用户还可以正确使用系统？
可用性可以通过增加硬件来改进：
  例如： 存储器中增加ECC
可靠性只能通过下列方法改进：
  改善使用环境状态
  建造更加可靠的元器件和部件
  减少系统使用的元器件和部件数
可以通过使用低成本、低可靠性的部件来改进可用性
Notes: This bring us to two terms that are often confused: reliability and availability.
Here is the proper distinction: reliability asks the question is anything broken?
Availability, on the other hand, ask the question is the system still availability to the user?
Adding hardware can therefore improve availability. For example, an airplane with two engines is more “available” than an airplane with one engine.
Reliability, on the other hand, can only be improved by bettering environmental conditions, building more reliable components, or reduce the number of components in the system.
Notice that by adding hardware to improve availability, you may actually reduce reliability.
For example, an airplane with two engines is twice as likely to have an engine failure than an airplane with only one engine so its reliability is lower although its availability is higher.
+2 = 44 min. (Y:24)

## Slide 43: 磁盘阵列
一种磁盘存储的新组织
  大量容量小、价廉的磁盘构成的阵列
  通过使用很多磁盘驱动器来提高潜在吞吐率:
    数据分布在多个磁盘上
    对不同磁盘进行多次访问
可靠性比单个磁盘更低
  但是可以通过增加冗余磁盘改进可用性，可以利用冗余信息重建丢失信息
  MTTR: 平均修复时间，小时级别
  MTTF: 平均无故障时间，三年至五年
Notes: The discussion of reliability and availability brings us to a new organization of disk storage where arrays of small and inexpensive disks are used to increase the potential throughput.
This is how it works: Data is spread over multiple disk so multiple accesses can be made to several disks either via interleaving or done in parallel.
While disk arrays improve throughput, latency is not necessary improved.
Also with N disks in the disk array, its reliability is only 1 over N the reliability of a single disk.
But availability can be improved by adding redundant disks so lost information can be reconstructed from redundant information.
Since mean time to repair is measured in hours and MTTF is measured in years, redundancy can make the availability of disk arrays much higher than that of a single disk.
+2 = 46 min. (Y:26)

## Slide 44: 网络存贮
磁盘大小逐步缩小
网络带宽逐步增加
网络文件服务
在高速网络上的
高性能
存贮服务
14" 10"  8"  5.25"  3.5"  2.5"  1.8"  1.3" . . .
基于磁盘阵列的高带宽磁盘系统
3 Mb/s  10Mb/s  50 Mb/s  100 Mb/s  1 Gb/s  10 Gb/s
网络的持续高带宽传输能力
网络提供了更好的
物理和逻辑接口：
独立的CPU 和
存贮系统！
支持远程文件访问的
操作系统 结构

## Slide 45: 磁盘阵列的制造上优势
14
10
5.25
3.5
3.5
磁盘阵列：
1种磁盘设计
常规：
4种磁盘设计
低端
高端
磁盘产品系列

## Slide 46: 阵列的可靠性
N个磁盘的可靠性 = 1个磁盘的可靠性  N
  50,000小时  70 磁盘 = 700 小时
磁盘系统的平均无故障时间：从 6 年 跌至 1个月！
没有冗余的阵列 在使用中 太不可靠！
可与访问过程 并行 进行重构的热备份：可以达到很高的媒体可用性

## Slide 47: 使用DRAM的二级存储
可以按两种方式使用DRAM作为第二级存储：
  固态盘（Solid state disk）
  扩展存储
固态盘：
  象磁盘一样进行操作，但是
    更快
    成本更高
  使用电池来保证系统信息不会丢失
扩展存储：
  允许数据块从主存移进和移出的较大存储器
Notes: One drawback of using magnetic disk as secondary storage is that it is slow.
There are two ways DRAM can be used for secondary storage: solid state disk and expanded storage.
Solid state disk behaves just like a disk except it is much faster because it does not have any delay caused by mechanical parts such as seek time and rotational delay.
The drawback of solid state disk is that it is very expensive.
Also, unlike disk which is non-volatile, DRAM will lost its contents if power is turned off so battery is used to make the system non-volatile.
As far as expanded storage is concerned, it is a large memory, much larger than the main memory, that only allows block transfers to or from main memory.
+2 = 48 min. (Y:28)

## Slide 48: 历史回顾
1956 IBM Ramac ~ 七十年代早期 Winchester
  针对大型机开发，专用接口
  在大小上不断缩小：27 in. 至 14 in.
七十年代
  5.25英寸软盘
  出现工业标准磁盘接口
    ST506, SASI, SMD, ESDI
八十年代早期
  个人计算机和第一代工作站
八十年代中期
  Client/server计算
  基于文件服务器的集中存储
    加速磁盘的小型化： 8英寸 至 5.25英寸
  巨大的磁盘驱动器市场成为现实
    工业标准： SCSI、IPI、IDE
    在PC市场，采用5.25英寸驱动器，专用接口寿终正寝

## Slide 49: 历史回顾
八十年代末/九十年代初：
  膝上机、笔记本电脑(掌上机)
  3.5英寸、 2.5英寸(1.8英寸)
  大小 加上 容量 驱动 市场，而非性能
    目前，带宽改进：40%/年
  来自DRAM、PCMCIA卡中flash RAM的挑战
    仍然太贵，Intel承诺降低成本但还没有兑现
    每立方英寸上兆字节，还不能另人满意
  光盘性能尚不理想，但有小的生存空间(CD ROM)

## Slide 50
CD
缺点
  是只读介质
优点：可移动
  制造成本低
  在大型存贮备份方面，具有与新型磁带技术竞争的潜力
光盘

## Slide 51
LCD

## Slide 52: Graphics Cards

## Slide 53: Polygons to Surfaces
数字坐标指定三维中的顶点位置
矩阵乘法将3D坐标转换为眼睛坐标
在透视图中将项目从3D划分为2D像素
处理器根据照明模型用适当的颜色填充多边形

## Slide 54: Sound
声音是空气压力的变化
麦克风将这些转换为模拟电信号
模数转换器以频繁的间隔对此进行采样, 生成的数字存储在文件（.wav）中播放时，数模转换器将这些数字转换为模拟电信号,扬声器的移动锥体将其转换为变化的空气压力

## Slide 55: 总线：将I/O与处理器和存储系统连接起来
总线是一组共享的通信链路
它使用一组线路将多个子系统连接起来
Control
Datapath
Memory
Processor
Input
Output
Notes: In a computer system, the various subsystems must be able to talk to one another. For example, the memory and processor need to communicate with each other.
Similarly, the processor needs to communicate with the I/O devices. The most common way to do is to use a bus.
A bus is a shared communication link that uses 1 set of wires to connect multiple subsystems.
+1 = 6 min. (X:46)

## Slide 56: 总线的优点
多功能性：
  易于增加新设备
  外设可在多个使用相同总线标准的计算机系统之间移动
低成本：
  可以以多种方式共享使用单一一组线路
Memory
Processor
I/O Device
I/O Device
I/O Device
Notes: The two major advantages of the bus organization are versatility and low cost.
By versatility, we mean new devices can easily be added.
Furthermore, if a device is designed according to a industry bus standard, it can be move between computer systems that use the same bus standard.
The bus organization is a low cost solution because a single set of wires is shared in multiple ways.
+1 = 7 min. (X:47)

## Slide 57: 总线的缺点
可能导致通信瓶颈
  总线的带宽制约了最大 I/O吞吐率
总线最高速度主要受制于：
  总线的长度
  总线上设备的数目
  需要支持多种设备的范围，特别是这些设备具有：
    时延差异很大
    数据传输率差异很大
Memory
Processor
I/O Device
I/O Device
I/O Device
Notes: The major disadvantage of the bus organization is that it creates a communication bottleneck. When I/O must pass through a single bus, the bandwidth of that bus can limit the maximum I/O throughput.
The maximum bus speed is also largely limited by:
(a) The length of the bus.
(b) The number of I/O devices on the bus.
(C) And the need to support a wide range of devices with a widely varying latencies and data transfer rates.
+2 = 9 min. (Y:49)

## Slide 58: 总线的典型组织
控制线：
  信号请求和应答
  指示数据线上的信息类型
数据线在源设备和目的设备之间传递信息:
  数据 和 地址
  复杂命令
一个总线事务 包括 两部分：
  发送地址
  接收 或 发送 数据
Data Lines
Control Lines
Notes: A bus generally contains a set of control lines and a set of data lines.
The control lines are used to signal requests and acknowledgments and to indicate what type of information is on the data lines.
The data lines carry information between the source and the destination.
This information may consists of data, addresses, or complex commands.
A bus transaction includes tow parts: (a) sending the address and (b) then receiving or sending the data.
+1 = 10 min (X:50)

## Slide 59: 主设备 与 从设备
一次总线事务 包括 两部分：
  发送地址
  接收 或 发送 数据
主设备（Master）是
  通过发送地址 来启始 总线事务 的设备
从设备 通过 下列过程对下述地址产生反应：
  如果主设备请求数据，就发送数据给主设备
  如果主设备要发送数据，就接收来自主设备的数据
Bus
Master
Bus
Slave
Master send address
Data can go either way
Notes: The bus master is the one who starts the bus transaction by sending out the address.
The slave is the one who responds to the master by either sending data to the master if the master asks for data.
Or the slave may end up receiving data from the master if the master wants to send data.
In most simple I/O operations, the processor will be the bus master but as I will show you later in today’s lecture, this is not always be the case.
+1 = 11 min. (X:51)

## Slide 60: 输出操作
这里输出是指处理器发送数据到I/O设备
处理器
控制 (存储器读请求)
存储器
第一步：请求存储器
I/O设备 (磁盘)
数据 (存储器地址)
处理器
控制
存储器
第二步：读存储器
I/O设备 (磁盘)
数据
Processor
控制(设备写请求)
存储器
第三步：向I/O设备发送数据
I/O设备 (磁盘)
数据
(I/O设备地址，
后跟数据)
Notes: We will define the term Output as the processor sending data to the I/O device and as shown here, it is a 3-step processes.
The first step is to wake up the memory by sending it a read request on the control line and the address of the location to be read on the data lines.
In the second step, the actual read occurs. That is the memory system is accessing the data.
Finally, the memory system transfers the data to the I/O device using the bus’s data lines and the control lines are used (either by the processor or by the memory system, depending on the memory system’s intelligence) to tell the I/O device data is coming.
+2 = 13 min. (X:53)

## Slide 61: 输入操作
这里输入是指处理器从I/O设备接收数据
处理器
控制(存储器写请求)
存储器
第一步：请求存储器
I/O设备 (磁盘)
数据 (存储器地址)
处理器
控制 (I/O读请求)
存储器
第二步：接收数据
I/O设备 (磁盘)
数据
(I/O设备地址，
后跟数据)
Notes: In our discussion, Input is defined as the processor receiving data from the I/O device and is only a 2-step process.
The first step is to wake up the Memory System by telling it a write operation is imminent (Control line) and provides the memory system with the address of the location to be written.
Then the CPU will tell the I/O device to start sending data by sending a read request to the I/O device (Control line and I/O address on the data line).
The data will then be sent to the Memory System via the data lines.
+1 = 54 min. (X:54)

## Slide 62: 总线类型
处理器-存储器总线 (面向设计)
  距离短、速度快
  仅需要与存储系统匹配
    可达最大存储器到处理器带宽
  直接与处理器相连
I/O总线(工业标准)
  通常，更长也更慢 需要与广泛的 I/O设备匹配
  与处理器-存储器总线或底板总线相连
单总线 ，又称底板总线(工业标准)
  底板（Backplane）：底盘（chassis）内的互联结构
  允许处理器、存储器和I/O设备共存
  成本优势：所有部件共享一条总线
Notes: Buses are traditionally classified as one of 3 types: processor memory buses, I/O buses, or backplane buses. The processor memory bus is usually design specific while the I/O and backplane buses are often standard buses.
In general processor bus are short and high speed. It tries to match the memory system in order to maximize the memory-to-processor BW and is connected directly to the processor.
I/O bus usually is lengthy and slow because it has to match a wide range of I/O devices and it usually connects to the processor-memory bus or backplane bus.
Backplane bus receives its name because it was often built into the backplane of the computer--it is an interconnection structure within the chassis.
It is designed to allow processors, memory, and I/O devices to coexist on a single bus so it has the cost advantage of having only one single bus for all components.
+2 = 16 min. (X:56)

## Slide 63: 具有单总线的计算机系统：底板总线
单总线（底板总线）用于：
  处理器 与 存储器 通信
  I/O设备 与 存储器 之间通信
优点：简单，成本低
缺点：速度慢，且总线可能是系统的主要瓶颈
示例： IBM PC
Processor
Memory
I/O Devices
Backplane Bus
Notes: Here is an example showing a single bus, the backplane bus is used to provide communication between the processor and memory.
As well as communication between I/O devices and memory.
The advantage here is of course low cost.
One disadvantage of this approach is that the bus with so many things attached to it will be lengthy and slow.
Furthermore, the bus can become a major communication bottleneck if everybody wants to use the bus at the same time.
The IBM PC is an example that uses only a backplane bus for all communication.
+2 = 18 min. (X:58)

## Slide 64: 双总线系统
I/O 总线通过总线适配器接入处理器-存储器总线：
  处理器-存储器总线：主要用于处理器-存储器之间的通信
  I/O总线：为 I/O设备提供扩展槽
Apple Macintosh-II
  NuBus：处理器、存储器，以及一些可选 I/O设备
  SCCI Bus：其他的I/O设备
Processor
Memory
I/O
Bus
Processor Memory Bus
Bus
Adaptor
Bus
Adaptor
Bus
Adaptor
I/O
Bus
I/O
Bus
Notes: Right before the break, I showed you a system with one bus only.
Here is an example using two buses where multiple I/O buses tap into the processor-memory bus via bus adaptors.
The Processor-memory bus is used mainly for processor-memory traffic while the I/O buses are used to provide expansion slots for the I/O devices.
The Apple Macintosh-II adopts this organization where the NuBus is used to connect processor, memory, and a few selected I/O devices together.
The rest of the I/O devices reside on an industry standard bus, the SCCI Bus, which is connected to the NuBus via a bus adaptor.
+2 = 25 min. (Y:05)

## Slide 65: 三总线系统
少量底板总线接入处理器-存储器总线
  处理器-存储器总线用于处理器-存储器之间的通信
  I/O总线连接到底板总线
优点：处理器总线上的负载急剧减少
Processor
Memory
Processor Memory Bus
Bus
Adaptor
Bus
Adaptor
Bus
Adaptor
I/O Bus
Backplane Bus
I/O Bus
Notes: Finally, in a 3-bus system, a small number of backplane buses (in our example here, just 1) tap into the processor-memory bus.
The processor-memory bus is used mainly for processor memory traffic while the I/O buses are connected to the backplane bus via bus adaptors.
An advantage of this organization is that the loading on the processor-memory bus is greatly reduced because of the small number of taps into the high-speed processor-memory bus.
+1 = 26 min. (Y:06)

## Slide 66: 同步 和 异步 总线
同步总线：
  在控制线中包括一个时钟线
  采用与时钟有关的一组固定通信协议
  优点：使用的逻辑非常少，可以以非常高的速度运行
  缺点：总线上的每个设备都必须以相同的时钟频率运行
    为了避免时钟扭斜，如果这种总线的速度很快，那么它就不能太长
异步总线：
  它没有时钟驱动 可以适用于很广泛的设备
  它很容易增长，而不需考虑时钟扭斜问题
  需要握手协议l
Notes: There are substantial differences between the design requirements for the I/O buses and processor-memory buses and the backplane buses.
Consequently, there are two different schemes for communication on the bus: synchronous and asynchronous.
Synchronous bus includes a clock in the control lines and a fixed protocol for communication that is relative to the clock.
Since the protocol is fixed and everything happens with respect to the clock, it involves very logic and can run very fast. Most processor-memory buses fall into this category.
Synchronous buses have two major disadvantages: (1) every device on the bus must run at the same clock rate. (2) And if they are fast, they must be short to avoid clock skew problem.
By definition, an asynchronous bus is not clocked so it can accommodate a wide range of devices at different clock rates and can be lengthened without worrying about clock skew.
The draw back is that it can be slow and more complex because a handshaking protocol is needed to coordinate the transmission of data between the sender and receiver.
+2 = 28 min. (Y:08)

## Slide 67: 握手协议
三条控制线
  ReadReq：指示对存储器有一次读请求
    同时，地址被放置在数据线上
  DataRdy：指示现在在数据线上的数据已经准备好
    同时，数据被放置在数据线上
  Ack：向另一方应答 ReadReq 或者 DataRdy
ReadReq
Address
Data
Data
Ack
DataRdy
1
2
2
3
4
4
5
6
6
7
处理器从存储器读数据
Notes: Here is a simple handshaking protocol example that uses three control lines:
(a) ReadReq indicates a read request for memory. When the sender asserts this signal, the address is put on the data lines at the same time.
(b) DataRdy indicates the data word is now ready on the data lines. When the data sender asserts this signal, it must also put the data on the data lines simultaneously.
(c) Ack is used to acknowledge the ReadReq or the DataRdy signal of the other party.
So here it is how it works. Assume the processor wants to read something from memory. The signal in red is driven by the processor while the signal in black is driven by memory.
(1) The processor initiates the bus transaction by asserting the ReadReq line and put the address it wants to read on the data lines at the same time.
(2) The memory upon seeing the ReadReq latch in the address asserts the Ack signal to (3) tell the processor: “I got it” so the it can disassert ReadReq as well as the Data lines.
(4) Upon seeing ReadReq goes low, the memory knows the processor is off the bus so it disasserts the Ack signal.
(5) When the data being requested is ready, the memory will put the data on the Data lines and asserts the DataRdy signal.
(6) Upon seeing the DataRdy signal, the processor will latch in the data on the data line and then assert the Ack to tell the memory it is now OK to get off the bus.
(7) Once the processor sees DataRdy line go low, it knows the memory has gotten off the bus so it disasserts the ACK signal so another bus transaction can start.
+3 = 31 min. (Y:11)

## Slide 68: 增加总线带宽
独立的 与 多路复用 的地址和数据线
  如果提供了独立的地址和数据线，那么就可以在一个总线周期同时传送地址和数据
  成本： (a) 需要更多的总线线路； (b) 增加复杂性
数据总线宽度：
  通过增加总线宽度，传输多个字的信息只需要较少的总线周期
  例如： SPARCstation 20的存储总线为128位宽
  成本：需要更多的总线线路
成块传输（Block transfers）
  允许总线在连续的多个总线周期传输多个字的信息
  仅仅在开始的时候需要提供一次地址
  总线在最后一个字传送完毕之前并不释放总线
  成本：(a) 增加了复杂性 (b)降低了请求的响应时间
Notes: Our handshaking example in the previous slide used the same wires to transmit the address as well as data. The advantage is saving in signal wires.
The disadvantage is that it will take multiple cycles to transmit address and data. By having separate lines for addresses and data, we can increase the bus bandwidth by transmitting address and data in the same cycle at the cost of more bus lines and increased complexity.
This (1st bullet) is one way to increase bus bandwidth. Another way is to increase the width of the data bus so multiple words can be transferred in a single cycle.
For example, the SPARCstation memory bus is 128 bits of 16 bytes wide. The cost of this approach is more bus lines.
Finally, we can also increase the bus bandwidth by allowing the bus to transfer multiple words in back-to-back bus cycles without sending an address or releasing the bus.
The cost of this last approach is an increase of complexity in the bus controller as well as a decease in response time for other parties who want to get onto the bus.
+2 = 33 min. (Y:13)

## Slide 69: 获得对总线的访问权
在总线设计中，最重要的一个论题：
  需要使用某总线的设备是如何获得并保留对该总线的使用权的？
通过主-从安排，可以避免混乱：
  只有总线主设备才能够控制对总线的访问：
    该主设备发起并控制所有的总线请求
  从设备对读和写请求发出响应
最简单的一个系统：处理器是唯一的总线主设备
  所有的总线请求都必须受到处理器的控制
  主要缺陷：在每次总线事务中都必须有处理器参与
Bus
Master
Bus
Slave
Control: Master initiates requests
Data can go either way
Notes: Taking about trying to get onto the bus: how does a device get onto the bus anyway? If everybody tries to use the bus at the same time, chaos will result.
Chaos is avoided by a maser-slave arrangement where only the bus master is allow to initiate and control bus requests.
The slave has no control over the bus. It just responds to the master’s response. Pretty sad.
In the simplest system, the processor is the one and ONLY one bus master and all bus requests must be controlled by the processor.
The major drawback of this simple approach is that the processor needs to be involved in every bus transaction and can use up too many processor cycles.
+2 = 35 min. (Y:15)

## Slide 70: 多个潜在总线主设备：需要仲裁
总线仲裁策略：
  希望使用总线的总线主设备发出总线请求
  该总线主设备在获得请求许可之前不能使用该总线
  该总线主设备在使用总线结束之后必须向仲裁器发出信号
总线仲裁策略通常需要平衡以下两个要素：
  总线优先权：最高优先权的设备必须被最先服务
  公平：即使是最低优先权的设备也不能永远得不到总线服务
总线仲裁策略大致可分为如下四类：
  基于自测的分布式仲裁：每个希望使用总线的设备都将代表自身的标志码放置在总线上；基于冲突监测的分布式仲裁：以太网使用该策略；菊花链（Daisy chain）仲裁 集中、并行仲裁
Notes: A more aggressive approach is to allow multiple potential bus masters in the system.
With multiple potential bus masters, a mechanism is needed to decide which master gets to use the bus next. This decision process is called bus arbitration and this is how it works.
A potential bus master (which can be a device or the processor) wanting to use the bus first asserts the bus request line and it cannot start using the bus until the request is granted.
Once it finishes using the bus, it must tell the arbiter that it is done so the arbiter can allow other potential bus master to get onto the bus.
All bus arbitration schemes try to balance two factors: bus priority and fairness. Priority is self explanatory. Fairness means even the device with the lowest priority should never be completely locked out from the bus.
Bus arbitration schemes can be divided into four broad classes. In the fist one:
(a) Each device wanting the bus places a code indicating its identity on the bus.
(b) By examining the bus, the device can determine the highest priority device that has made a request and decide whether it can get on.
In the second scheme, each device independently requests the bus and collision will result in garbage on the bus if multiple request occurs simultaneously.
Each device will detect whether its request result in a collision and if it does, it will back off for an random period of time before trying again.
The Ethernet you use for your workstation uses this scheme.
We will talk about the 3rd and 4th schemes in the next two slides.
+3 = 38 min. (Y:18)

## Slide 71: 菊花链总线仲裁策略
优点：简单
缺点：
  不能保证公平：低优先级的设备可能永远得不到服务
  grant信号会限制总线的速度
Bus
Arbiter
Device 1
Highest
Priority
Device N
Lowest
Priority
Device 2
Grant
Grant
Grant
Release
Request
Notes: The daisy chain arbitration scheme got its name from the structure for the grant line which chains through each device from the highest priority to the lowest priority.
The higher priority device will pass the grant line to the lower priority device ONLY if it does not want it so priority is built into the scheme.
The advantage of this scheme is simple. The disadvantages are:
(a) It cannot assure fairness. A low priority device may be locked out indefinitely.
(b) Also, the daisy chain grant line will limit the bus speed.
+1 = 39 min. (Y:19)

## Slide 72: 使用单一总线仲裁器的集中式仲裁
Arbiter
Highest priority: ReqA
Lowest Priority: ReqC
Clk
ReqA
ReqB
ReqC
GrantA
GrantB
GrantC
Clk
ReqA
ReqB
GrA
GrB
Notes: In the centralized, parallel arbitration scheme, the devices independently request the bus by using multiple request lines.
A centralized arbiter chooses from among the devices requesting bus access and notifies the selected device that it is now the bus master via one of the grant line.
Here is an example with A has the highest priority and C the lowest. Since A has the highest priority, Grant A will be asserted even though both requests A and B are asserted.
Device A will keep Request A asserted until it no longer needs the bus so when Request A goes low, the arbiter will disassert Grant A.
Since Request B remains asserted (Device B has not gotten the bus yet) at this time, the arbiter will then asserts Grant B to grant Device B access to the bus.
Similarly, Device B will not disassert Request B until it is done with the bus.
+2 = 41 min. (Y:21)

## Slide 73: 总线小结
三种类型总线：
  处理器-存储器总线
  I/O总线
  底板总线
总线总裁策略：
  菊花链仲裁：不能保证公平性
  集中并行仲裁：需要中央仲裁器
I/O设备通报操作系统：
  轮询:浪费一些处理器时间
  I/O中断：与一些意外事件类似，只是它是异步的
把CPU从I/O处理中解放出来
  Direct memory access (DMA)
  I/O processor (IOP)
Notes: Let’s summarize what we learned today. First we talked about three types of buses: the processor-memory bus, which is usually the shortest and fastest.
The I/O bus, which has to deal with a large range of I/O devices, is usually the longest and slowest. The backplane bus is a general interconnect built into the chassis of the machine.
The processor-memory bus, which runs at high speed, usually is synchronous while the I/O and backplane buses can either be synchronous or asynchronous.
As far as bus arbitration schemes are concerned, I showed you two in details. The daisy chain scheme is simple, but it is slow and cannot assure fairness--that is a low priority device may never get to use the bus at all.
The centralized parallel arbitration scheme is faster but it requires a centralized arbiter so I also show you how to build a simple arbiter using simple AND gates and JK flip flops.
When we talked about OS’s role, we discussed two ways an I/O device can notify the operating system when data is ready or something goes wrong.
Polling is simple to implement but it may end up wasting a lot of processor cycle.
I/O interrupt is similar to exception but it is asynchronous with respect to instruction execution so we can pick our own convenient point in the pipeline to handle it.
Finally we talked about two ways you can delegate I/O responsibility from the CPU: Direct memory access and IO processor.
+3 = 77 min. (Y:57)

## Slide 74: That’s it folks!
You now have a pretty good idea about:
How computers are designed and how they work
  How data and instructions are represented
  How arithmetic and logic operations are performed
  How ALU and control circuits are implemented
  How registers and the memory hierarchy are implemented
  How performance is measured
  How performance is increased via pipelining, caching
  How VM works.
  (briefly) What the rest of the computer looks like (disks, sound, etc.)